## Slide 1: 21st Century Reversal of the Surface Ozone Seasonal Cycle over the Northeastern United States
Olivia Clifton
GloDecH Meeting May 28, 2014
Acknowledgments. Arlene Fiore (CU/LDEO), Gus Correa (LDEO), Larry Horowitz (NOAA/GFDL), Vaishali Naik (UCAR/GFDL)
83520601
Lower Manhattan, 1948
Image Credit: Unknown

## Slide 2: Surface Ozone (O3): degrades air quality & is injurious to human health and vegetation
Surface O3 = NOx + sunlight +
Non-methane volatile organic compounds (NMVOCs)
Methane (CH4)
Carbon Monoxide (CO)
Notes: Surface O3 forms through the photochemical oxidation of methane, non-methane volatile organic compounds (NMVOCs), or carbon monoxide (CO) in the presence of sunlight and nitrogen oxides (NOx).

## Slide 3: Surface O3 levels controlled by nonlinear chemistry
NOx-limited
Ridge
NOx-saturated
Reductions in NOx emissions achieve local-to-regional decreases in surface O3 and reductions in CH4 emissions lower the surface O3 everywhere [Fiore et al., 2002]
In highly polluted regions (very high regional NOx), NOx can destroy surface O3
OZONE CONCENTRATIONS vs. NOx & VOC EMISSIONS
Notes: Surface ozone levels are controlled by nonlinear chemistry
Ridge separates two photochemical regimes
NOx-limited: ozone increases with rising NOx, but remains relatively unchanged for increasing VOCs
NOx-saturated: ozone increases with increasing VOC and decreases with increasing NOx
Some background to keep in mind

## Slide 4: Seasonal cycle of observational surface O3 at NE monitoring sites during 1991-1996
Feb Apr Jun Aug Oct Dec
mean across 3 regionally representative Clean Air Status and Trends Network (CASTNet) sites [Reidmiller et al., 2008]
Regionally
representative site (each site has 4-6 years of observations)
Washington Crossing, NJ
Penn State, PA
Connecticut Hill, NY

## Slide 5: Seasonal cycle of observational surface O3 at NE monitoring sites during 1991-1996
Feb Apr Jun Aug Oct Dec
mean across 3 regionally representative Clean Air Status and Trends Network (CASTNet) sites [Reidmiller et al., 2008]
Highest surface O3 during the summer due to presence of precursor emissions (both NOx and VOCs) and favorable meteorological conditions (i.e. high temperatures, low cloud cover, and stagnation)
Regionally
representative site
Densely populated and highly polluted region

## Slide 6: Change in seasonal cycle of observational surface O3 over NE due to a 26% decrease in regional NOx emissions
Solid: 1991-1996, pre-NOx emission controls
Dashed: 2004-2009, post-NOx emission decreases
-26% NE NOx
Feb Apr Jun Aug Oct Dec
Regionally
representative site
mean across 3 regionally representative Clean Air Status and Trends Network (CASTNet) sites [Reidmiller et al., 2008]
Notes: Ok some this is the same plot as before but I’ve added a new seasonal cycle, the dashed line, which corresponds to 2004-2009
Between these two time periods there were 26% decreases in regional Nox emissions

## Slide 7: Change in seasonal cycle of observational surface O3 over NE due to a 26% decrease in regional NOx emissions
Solid: 1991-1996, pre-NOx emission controls
Dashed: 2004-2009, post-NOx emission decreases
Feb Apr Jun Aug Oct Dec
How will the surface O3 seasonal cycle over the NE US respond to further regional as well as global precursor emission changes during the rest of 21st C?
Regionally
representative site
-26% NE NOx
mean across 3 regionally representative Clean Air Status and Trends Network (CASTNet) sites [Reidmiller et al., 2008]

## Slide 8: GFDL CM3 chemistry-climate model is the tool that we use to project 21st C surface O3
Donner et al. [2011]; Golaz et al. [2011]; Levy et al. [2013]; Naik et al. [2013]; Austin et al. [2013]; John et al. [2012]
cubed sphere grid
~2°x2°
48 vertical levels
Atmospheric Dynamics & Physics
Radiation, Convection (includes wet deposition of tropospheric species), Clouds, Vertical diffusion, and Gravity wave
Chemistry of gaseous species (O3, CO, NOx, hydrocarbons) and aerosols (sulfate, carbonaceous, mineral dust, sea salt, secondary organic)
Dry Deposition
Aerosol-Cloud Interactions
Chemistry of Ox, HOy, NOy, Cly, Bry, and Polar Clouds in the Stratosphere
Forcing
Solar Radiation
Well-mixed Greenhouse Gas Concentrations
Volcanic Emissions
Ozone–Depleting Substances (ODS)
Modular Ocean Model version 4 (MOM4)
&
Sea Ice Model
Pollutant Emissions (anthropogenic, ships, biomass burning, natural, & aircraft)
Land Model version 3
(soil physics, canopy physics, vegetation dynamics, disturbance and land use)
GFDL-CM3
GFDL-CM3
Atmospheric Chemistry
86km
c/o V. Naik
Notes: So GFDL CM3 is the tool that we use to project 21st Century surface ozone.
I would like to point out that CM3 is a chemistry-climate model that includes online fully coupled tropospheric and stratospheric chemistry including gas phase and aerosols within an atmosphere-ocean GCM.

## Slide 9: Evaluation of CM3 with observational surface O3 over NE
-10% IMW NOx
Feb Apr Jun Aug Oct Dec
-26% NE NOx
Solid: 1991-1996, pre-NOx emission controls
Dashed: 2004-2009, post-NOx emission decreases
OBS CM3
mean across 3 regionally representative CASTNet sites [Reidmiller et al., 2008]
Regionally
representative site
3 Ensemble member mean
Notes: Ok now the same plot as before, but with model seasonal cycles for the same time periods
Captures small increases during winter and early spring and small decreases during summer

## Slide 10: Evaluation of CM3 with observational surface O3 over NE
-10% IMW NOx
Feb Apr Jun Aug Oct Dec
-26% NE NOx
Solid: 1991-1996, pre-NOx emission controls
Dashed: 2004-2009, post-NOx emission decreases
OBS CM3
Despite high bias, CM3 captures the overall structure of the seasonal surface O3 changes over the NE & thus the response of surface O3 to the NOx emission controls
mean across 3 regionally representative CASTNet sites [Reidmiller et al., 2008]
Regionally
representative site
3 Ensemble member mean

## Slide 11: Evaluation of CM3 with observational surface O3 over NE
-10% IMW NOx
Feb Apr Jun Aug Oct Dec
-26% NE NOx
Solid: 1991-1996, pre-NOx emission controls
Dashed: 2004-2009, post-NOx emission decreases
OBS CM3
We conclude that we can use CM3 to determine how surface O3 will respond to future precursor emission changes
Despite high bias, CM3 captures the overall structure of the seasonal surface O3 changes over the NE & thus the response of surface O3 to the NOx emission controls
mean across 3 regionally representative CASTNet sites [Reidmiller et al., 2008]
Regionally
representative site
3 Ensemble member mean
Notes: One possible explanation for the model bias is that in the real world, precursor emission controls were imposed most strongly during the surface ozone season, whereas we do not have seasonally varying anthropogenic emissions in CM3.

## Slide 12: Month of peak monthly mean surface O3 (3 ensemble member mean)
2006-2015
Feb Apr Jun Aug Oct Dec
Notes: So now we jump to looking at the 21st Century projections. So this plot shows the month holding the peak monthly mean surface ozone over the united states during one of the first decades of the 21st Century. We see that over the eastern united states, peak monthly mean ozone occurs during the summer. On the other hand, the peak occurs over the rest of the US during cooler months. We expect this dichotomy because of the combination of regional NOx emissions and favorable meteorological conditions characteristic of the eastern US during summer.

## Slide 13: Month of peak monthly mean surface O3 (3 ensemble member mean)
2006-2015
2091-2100
Clear shift in the peak from summer to winter/early spring over Eastern US
Feb Apr Jun Aug Oct Dec
Notes: Conclusion: clear shift….
--------
The high elevation, deep boundary layer, and long O3 lifetime characteristic of the IMW lead to higher levels of mean background O3 than in the Eastern US [Fiore et al., 2002; Jaffe, 2011; Zhang et al., 2011]. Over the Western US, background O3 typically peaks during the spring, due to the long O3 lifetime and the seasonal peak in stratospheric influence [e.g. Wang et al., 1998].

## Slide 14: Month of peak monthly mean surface O3 (3 ensemble member mean)
2006-2015
2091-2100
Clear shift in the peak from summer to winter/early spring over Eastern US
Feb Apr Jun Aug Oct Dec
Under RCP8.5
RCPs created in conjunction with IPCC AR5 and CMIP5
Designed to attain a specific RF (8.5 W/m2) by 2100
The most extreme 21st C Climate scenario with doubling of global CH4 abundance by 2100
Notes: So this projection of surface ozone is under a 21st century climate scenario called RCP8.5

## Slide 15: Month of peak monthly mean surface O3 (3 ensemble member mean)
2006-2015
Under RCP8.5
RCPs developed by CMIP effort in support of IPCC
Designed to attain a specific RF (8.5 W/m2) by 2100
The most extreme 21st C Climate scenario with doubling of global CH4 abundance by 2100
2091-2100
Clear shift in the peak from summer to winter/early spring over Eastern US
Investigate the drivers of this shift over NE (drastic regional NOx emission decreases, changes in global CH4 abundance, increased climate warming, or some combination?) by examining the change in seasonal cycle at beginning & end of 21st C
Evaluate the magnitude of the change in surface O3 & the change in shape of seasonal cycle
Compare RCP8.5 with RCP4.5 (moderate; 10% decrease of global CH4) as well as with sensitivity simulations
Feb Apr Jun Aug Oct Dec

## Slide 16: Surface O3 seasonal cycle at beginning and end of the 21st C under RCP4.5 and RCP8.5
-90% NE NOx
-90% NE NOx
-10% global CH4
+114% global CH4
Feb Apr Jun Aug Oct Dec
Each symbol is ensemble member; lines are ensemble member mean (3)
Notes: These seasonal cycles are over the NE as the previous slide, but monthly mean surface ozone is averaged across all the gridboxes that fall in the regional domains, instead of across a couple of regionally representative sites.
the changes in global methane abundance are in the upper right corner of the plot and the changes in regional nox emissions are in the lower left corner.
The black seasonal cycles correspond to the beginning of century and black triangles represent rcp4.5 and black circles are rcp8.5. surface O3 peaks during the summer with a smaller peak during March
Red seasonal cycle corresponds to RCP8.5 at 2100 and the blue seasonal cycle corresponds to RCP4.5 at 2100.
the 2100 seasonal cycles have different magnitudes under RCP4.5 and under RCP8.5, reflecting the different emission scenarios, but the seasonal cycles have similar shape with maxima during cooler months

## Slide 17: Surface O3 seasonal cycle at beginning and end of the 21st C under RCP4.5 and RCP8.5
-90% NE NOx
-90% NE NOx
NE resembles baseline O3 conditions by end of 21st C [NRC, 2009; Parrish et al., 2013]
Reversal of the NE surface O3 seasonal cycle during 21st C after 2020s (not shown)
-10% global CH4
+114% global CH4
Feb Apr Jun Aug Oct Dec
Notes: This indicates two conclusions: that the NE becomes representative of baseline O3 conditions and that there is a clear reversal of the seasonal cycle over the NE by 2100.

## Slide 18: Surface O3 seasonal cycle at beginning and end of the 21st C under RCP8.5 and a sensitivity simulation holding all CH4 at 2005 levels
Feb Apr Jun Aug Oct Dec Feb Apr Jun Aug Oct Dec
-90% NE NOx +114% global CH4
-90% NE NOx +0% global CH4
The doubling of global methane abundance raises the entire seasonal cycle by about 6-11 ppb, with the greatest differences between RCP8.5 and RCP8.5_2005CH4 during January through March when the O3 lifetime is longest

## Slide 19: Surface O3 seasonal cycle at beginning and end of the 21st C under RCP8.5 and a sensitivity simulation holding all CH4 at 2005 levels
-90% NE NOx +114% global CH4
-90% NE NOx +0% global CH4
Reduced NOx emissions play a role in increasing surface O3 during the winter in highly polluted regions [US EPA, 2014]
While NOx exerts a dominant influence on the shape of the surface O3 seasonal cycle, global CH4 abundance influences the baseline surface O3 abundance during all months
Feb Apr Jun Aug Oct Dec

## Slide 20: Rising baseline surface O3 by 2100 from increases in global CH4 abundance
RCP8.5_2005CH4_rad 2091-2100 same as RCP8.5 2091-2100 (not shown)
RCP8.5_2005CH4_chem (dashed) 2091-2100 same as RCP8.5_2005CH4 2091-2100
- 43% IMW NOx
The CH4 impact on surface O3 in the model occurs mainly though atmospheric chemistry, rather than through the additional climate forcing from CH4
Feb Apr Jun Aug Oct Dec
NE US 36-46 N 80-70W IMW US 36-46N 115-105W
- 90% NE NOx
Notes: 0.62 historical
4.42 rcp85
3.15 rcp85_wmgg
3.47 rcp85_2005ch4
4.03 rcp85_2005ch4_chem
3.93 rcp85_2005ch4_rad
2.24 rcp45
1.4 rcp4.5_wmgg

## Slide 21: Impact of a warming climate on the surface O3 seasonal cycle
Feb Apr Jun Aug Oct Dec
RCP4.5_WMGG & RCP8.5_WMGG isolate impacts from a changing climate
JJA NE temp inc. by 5.5ºC
JJA NE temp inc. by 2.5ºC
Same findings under RCP4.5_WMGG & RCP8.5_WMGG, but magnitude of each change depends on the regional temperature increases
Notes: WMGG simulations hold all o3 precursors at 2005 and only well mixed green house gases are allowed to evolve to 2100 levels.

## Slide 22: Impact of a warming climate on the surface O3 seasonal cycle
Feb Apr Jun Aug Oct Dec
RCP4.5_WMGG & RCP8.5_WMGG isolate impacts from a changing climate
JJA NE temp inc. by 5.5ºC
JJA NE temp inc. by 2.5ºC
General increases in summertime surface O3 over NE reflect “Climate change penalty”
Wu et al., 2008
need for stricter emission controls to achieve a given level of air quality due to warming climate (but in absence of precursor emission changes)

## Slide 23: Impact of a warming climate on the surface O3 seasonal cycle
Feb Apr Jun Aug Oct Dec
RCP4.5_WMGG & RCP8.5_WMGG isolate impacts from a changing climate
JJA NE temp inc. by 5.5ºC
JJA NE temp inc. by 2.5ºC
Climate change penalty predominantly affects surface O3 during the photochemically active season, May-September, in regions with sufficiently high anthropogenic NOx emissions
Broadening of the summertime peak over the NE with similar levels of surface O3 in June-August, as opposed to a clear peak in July
Notes: And so we also see a broadening ..
So we conclude …

## Slide 24: Conclusions
Reversal of NE US high-surface O3 season
Changing regional emissions alters high surface O3 season
Climate change broadens surface O3 peak in NE US
Rising global CH4 can offset O3 decreases from U.S. precursor reductions
NE at end of 21st C more representative of baseline O3 conditions
Questions?